Inspected by: _______________________________________ 			 						Date: ________________

- Do workers know appropriate anchorage points for each task that requires a fall-arrest or restraint system? __________

- Are all anchorage points stable, substantial, and have sufficient strength to withstand twice the potential impact energy of the free-fall? __________

- Are all anchorage points for body harnesses located at shoulder height?	__________

- Are anchorage points for self-retracting lifeline systems located overhead? __________

- Can a worker move from one station to another or climb up and down without exposure to a fall? __________

- If the lifeline, lanyard, or self-retracting lifeline is not permanently attached to an anchorage point at the elevated work area, is the first worker up or the last worker down protected while climbing and traversing? __________

ANCHORAGE POINTS

- A minimum breaking strength of 22 kN non-engineered or 2 times maximum arresting force anticipated, for engineered anchorage point?  _________

- Is the lifeline protected from abrasive or cutting edges? __________

- Does the system provide fall protection as the worker connects to and releases from the lifeline? _________

- Is the lifeline arranged so workers never have to hold it for balance? (a lifeline should never be used for balance) _________

HORIZONTAL & VERTICAL LIFELINES

- Has the entire horizontal lifeline system been designed and approved by a competent person (CSA Z259.13 & CSA Z259.16)? _________

- Have the anchorages to which the lifeline is attached been designed and evaluated specifically for a horizontal lifeline? __________

- Has the designer of the system approved the number of workers who will be using it? _________

- Is the rope or cable free from signs of wear or abrasion? __________

- Does the rope or cable have the required initial sag? __________

- Have the workers been warned about potential falls? __________

- Have the clearances been checked? _________

- Is the hardware riding on the horizontal lifeline made of steel? (aluminum is not permitted because it wears excessively) __________

- Is the vertical segment integrated with the horizontal segment to provide continuous fall protection (CSA Z259.2.1)? __________

FALL ARRESTERS

- Is the fall arrester compatible with the lifeline on which it is to be installed or operated? _________

- Is the fall arrester in operational condition? __________

- Is the fall arrester equipped with a changeover lever that allows it to become a stationary anchor on the lifeline? __________

- Is the fall arrester equipped with a locking mechanism that prevents unintentional opening of the device and disengagement from the lifeline? ______

- Is the fall arrester’s “up” direction marked properly so that the equipment can be attached to the line correctly? __________

- Is the fall arrester included in a regular maintenance program? __________

LANYARDS

- Is the lanyard length as short as necessary and in no case greater than 6 feet? (1.8 meters) __________

- Are manually adjustable lanyards used when it is desirable to be able to take slack out of the lanyard? __________

- Does the lanyard have a shock-absorbing feature to limit the arresting forces to 500-600 pounds? (227- 272 kilograms) ___________

- If the lanyard has a shock absorber, is it obvious to the user that the shock absorber has been deployed? (Is there a warning label, broken pouch, etc.) __________

- Have you prohibited tying of knots from the lanyard to the lifeline? (mechanical rope grabs or fall arresters must be used) ___________

RETRACTABLE LIFELINE (CSA Z259.2.2)

- Are workers properly trained to use an RL? ___________

- Is the RL under a regular maintenance and inspection program? ___________

- Is the end of the cable properly spliced? ___________ (Thimble eye, Flemish eye-spliced, and swaged fitting/ferrule)

- Minimizes hazard of swinging? ___________

- Limits the distance they drop during the swing to 1.2 meters? ___________

SNAP HOOKS

- Have double-locking snap hooks been used? ___________

- Is the snap hook attached to the D-ring, eyebolt, or other hardware in a manner approved by the manufacturer of the snap hook? ___________

- Are snap hooks inspected regularly for stress, wear, distortion, and spring failure? __________

- Are snap hooks arranged so they are never connected to each other? __________

BODY HARNESSES

- Are full-body harnesses selected (CSA Z259.10) for a particular job equipped with all necessary attachment points? (for fall arresting, work positioning, descent control, rescue, or ladder fall-protection systems) __________

- Are body harnesses inspected regularly for wear, abrasion, broken stitching, and missing hardware? ___________

- Is the Velcro type of closure prohibited from all load-bearing connections? __________

- Have workers been instructed in the use and care of body harnesses/body belts? __________

OTHER CONSIDERATIONS

- Has the free-fall distance been considered, so that a worker will not strike a lower surface or object before the fall is arrested? _____________

- Have pendulum-swing fall hazards been eliminated? _____________

- Have safe methods to retrieve fallen workers been planned? ____________

- Is all fall-arrest equipment free of potential damage from welding, chemical corrosion, or sandblasts? __________

- Are all components of the system compatible according to the manufacturer’s instruction? __________

- Have employees been properly trained in the following issues?

- Manufacturer’s recommendations, restrictions, instructions, and warnings _____________

- Location of appropriate anchorage points and attachment techniques _____________

- Problems associated with elongation, deceleration distance, method of use, inspection, and storage __________

- Are all regular inspections performed by trained inspectors? ____________

- Are written reports maintained? __________